Title
An Introduction to CDMA
Spread-Spectrum
© 2010-2019 Nick Waterman VA3NNW

---
Overview
An Introduction to CDMA
- CDMA is a coding scheme used in many 3G/4G/5G cellular networks
- There will be SOME math

---
An Introduction to CDMA
- CDMA is a coding scheme used in many 3G/4G/5G cellular networks
- There will be SOME maths

---
An Introduction to CDMA
- CDMA is a coding scheme used in many 3G/4G/5G cellular networks
- There will be SOME maths, but quite easy (x and +)

---
CDMA?
What does it stand for?
- Code
- Division
- Multiple
- Access

---
Multiple Access?

---
Overview
FDMA
- Frequency
- Division
- Multiple
- Access

---
FDMA

---
FDMA
(1G Cellular Networks)

---
TDMA
- Time
- Division
- Multiple
- Access

---
TDMA

---
F/TDMA
- Frequency and Time
- Division
- Multiple
- Access

---
F/TDMA
(2G Cellular Networks)

---
F/TDMA
Ham Bands

---
CDMA
- CODE
- Division
- Multiple
- Access
?

---
CDMA

---
CDMA
Uses the whole band, for the whole time
(Scares the ҨӁɜʨѪ out of the CW narrow-bandwidth fans)

---
CDMA
Everyone transmits on top of everyone else.
How do we show this?

---
CDMA
Some people show it like this...
… but I prefer

---
CDMA
(3G, 4G, 5G Cellular Networks)

---
CDMA
(3G, 4G, 5G Cellular Networks)

---
… but you're probably wondering...

---
Hang on,
Everyone transmits on top of each other?
Across the whole band?
At the same time?

---
YES.
With different codes,
and if you know the right code, you can receive just the person transmitting with that code.

---
Err, OK...
So how do we make it?
First, a bit of a reminder:
AM and SSB

---
Frequency Spectrum

---
Voice

---
Voice, Carrier
→
… and mix ...

---
AM
… or SSB ...

---
SSB

---
Let's do the same for CDMA:

---
Data Signal
… and a very wideband spreading code ...

---
Data Signal + Code
→
… and mix ...

---
CDMA
… to make really wideband CDMA spread spectrum signal
… but we can also turn the power down ...

---
CDMA
… right down ...

---
CDMA
… below the noise floor!
… and still be heard!
Trust me. We'll prove it later.

---
… and the hardware?
What does that look like?
Let's again compare with SSB:

---
SSB Transceiver Block Diagram

---
CDMA Transceiver Block Diagram
Except this is usually mostly digital, so...

---
CDMA Transceiver Block Diagram

---
Can we walk through an example?

---
WARNING! Here comes the maths!
… but it's quite simple multiplication
… though it does include negative numbers.
Don't worry, my kids did it at age 8 :-)

---
Multiplication
 1
x
 1
=
 1
 1
x
-1
=
-1
-1
x
 1
=
-1
-1
x
 -1
=
 1

---
CDMA example
Low-Bandwidth Signal:
High-Bandwidth Spreading Code:
...repeated...

---
CDMA example
Low-Bandwidth Signal:
High-Bandwidth Spreading Code:
Mix is a simple multiply
… and transmit.

---
CDMA example
To Decode / Receive, take the signal:

---
CDMA example
To Decode / Receive, take the signal:
Multiply by the same Spreading Code:
… to get ...
… which you should recognise as...

---
CDMA example
To Decode / Receive, take the signal:
Multiply by the same Spreading Code:
… to get ...

---
(Discuss noise)
To Decode / Receive, take the signal:
Multiply by the same Spreading Code:
… to get ...

---
What if we use the wrong code?
Take the same signal:
Multiply by the wrong Spreading Code:

---
What if we use the wrong code?
Take the same signal:
Multiply by the wrong Spreading Code:
… for example, let's just shift the same code left a bit:

---
What if we use the wrong code?
Take the same signal:
Multiply by the wrong Spreading Code:
… for example, let's just shift the same code left a bit:

---
What if we use the wrong code?
Take the same signal:
Multiply by the wrong Spreading Code:
… you get ...
… which clearly hasn't recovered the original signal.
Using wrong code is like being off-frequency.

---
This obviously shows that
timing is critical. To receive a signal, you not only need to be generating the RIGHT code, but your TIMING needs to be locked very tightly to the
received signal too.
More on that later if I have time.

---
A more serious example:
Audience Participation!

---
Audience Participation
Data
x
Spreading Code
=
CDMA

---
Audience Participation
- LEFT side of room:
- Take some “data”
  (pick a letter)
- Multiply by Spreading Code A
- “Transmit” CDMA to me
- RIGHT side of room:
- Take some “data”
  (pick a letter)
- Multiply by Spreading Code B
- “Transmit” CDMA to me
2 volunteers will make some NOISE :-)
I will add LEFT+RIGHT+NOISE to see what might be received
on the band

---
Audience Participation
- LEFT side of room:
- Multiply by Spreading Code B
- “Receive” CDMA from RIGHT
- RIGHT side of room:
- Multiply by Spreading Code A
- “Receive” CDMA from LEFT
… and with some luck, it'll work!
I will add LEFT+RIGHT+NOISE to see what might be received

---
First, pick a letter. Write it in Box 1
Letter
A
B
C
D
E
F
G
H
I
J
K
L
M
Letter
N
O
P
Q
R
S
T
U
V
W
X
Y
Z

---
Now copy Data into boxes 2-6
Letter	Data
	2	3	4	5	6
A	1	1	1	1	1
B	1	1	1	1	-1
C	1	1	1	-1	1
D	1	1	1	-1	-1
E	1	1	-1	1	1
F	1	1	-1	1	-1
G	1	1	-1	-1	1
H	1	1	-1	-1	-1
I	1	-1	1	1	1
J	1	-1	1	1	-1
K	1	-1	1	-1	1
L	1	-1	1	-1	-1
M	1	-1	-1	1	1
Letter	Data
	2	3	4	5	6
N	1	-1	-1	1	-1
O	1	-1	-1	-1	1
P	1	-1	-1	-1	-1
Q	-1	1	1	1	1
R	-1	1	1	1	-1
S	-1	1	1	-1	1
T	-1	1	1	-1	-1
U	-1	1	-1	1	1
V	-1	1	-1	1	-1
W	-1	1	-1	-1	1
X	-1	1	-1	-1	-1
Y	-1	-1	1	1	1
Z	-1	-1	1	1	-1

---
Example TX
Data	1					-1
x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x
Spreading Code	1	-1	1	-1	-1	1	-1	1	1	-1	1	-1	-1	1	-1	1
=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=
CDMA
2
3

---
Example TX
Data	1					-1
x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x
Spreading Code	1	-1	1	-1	-1	1	-1	1	1	-1	1	-1	-1	1	-1	1
=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=
CDMA	1

---
Example TX
Data	1					-1
x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x
Spreading Code	1	-1	1	-1	-1	1	-1	1	1	-1	1	-1	-1	1	-1	1
=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=
CDMA	1	-1

---
Example TX
Data	1					-1
x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x
Spreading Code	1	-1	1	-1	-1	1	-1	1	1	-1	1	-1	-1	1	-1	1
=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=
CDMA	1	-1	1	-1	-1	1	-1	1

---
Example TX
Data	1					-1
x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x
Spreading Code	1	-1	1	-1	-1	1	-1	1	1	-1	1	-1	-1	1	-1	1
=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=
CDMA	1	-1	1	-1	-1	1	-1	1	-1

---
Example TX
Data	1					-1
x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x
Spreading Code	1	-1	1	-1	-1	1	-1	1	1	-1	1	-1	-1	1	-1	1
=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=
CDMA	1	-1	1	-1	-1	1	-1	1	-1	1

---
Example TX
Data	1					-1
x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x
Spreading Code	1	-1	1	-1	-1	1	-1	1	1	-1	1	-1	-1	1	-1	1
=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=
CDMA	1	-1	1	-1	-1	1	-1	1	-1	1	-1	1	1	-1	1	-1
7

---
(Step 7)
Data
x Spreading Code
= CDMA
 1
x
 1
=
 1
 1
x
-1
=
-1
-1
x
 1
=
-1
-1
x
 -1
=
 1

---
Step 8: A + B + Noise = Band
CDMA / A	1	-1	1	-1	-1	1	-1	1	-1	1	-1	1	1	-1	1	-1
+	+	+	+	+	+	+	+	+	+	+	+	+	+	+	+	+
CMDA / B	1	-1	-1	1	-1	1	1	-1	-1	1	1	-1	1	-1	-1	1
+	+	+	+	+	+	+	+	+	+	+	+	+	+	+	+	+
NOISE	3	2	3	2	5	5	3	2	5	4	5	4	2	4	5	5
=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=
BAND

---
Step 8: A + B + Noise = Band
CDMA / A	1	-1	1	-1	-1	1	-1	1	-1	1	-1	1	1	-1	1	-1
+	+	+	+	+	+	+	+	+	+	+	+	+	+	+	+	+
CMDA / B	1	-1	-1	1	-1	1	1	-1	-1	1	1	-1	1	-1	-1	1
+	+	+	+	+	+	+	+	+	+	+	+	+	+	+	+	+
NOISE	3	2	3	2	5	5	3	2	5	4	5	4	2	4	5	5
=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=
BAND	5	0	3	2	3	7	3	2	3	6	5	4	4	2	5	5

---
Example RX
BAND	5	0	3	2	3	7	3	2	3	6	5	4	4	2	5	5
x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x
Spreading Code	1	-1	1	-1	-1	1	-1	1	1	-1	1	-1	-1	1	-1	1
=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=
Demod	5
Add these	└───────┬───────┘ / +								└───────┬───────┘ / +
Total
1 or -1?
9
10

---
Example RX
BAND	5	0	3	2	3	7	3	2	3	6	5	4	4	2	5	5
x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x
Spreading Code	1	-1	1	-1	-1	1	-1	1	1	-1	1	-1	-1	1	-1	1
=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=
Demod	5	0	3	-2	-3	7	-3	2	3	-6	5	-4	-4	3	-5	5
Add these	└───────┬───────┘ / +								└───────┬───────┘ / +
Total
1 or -1?
10
11

---
Example RX
BAND	5	0	3	2	3	7	3	2	3	6	5	4	4	2	5	5
x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x
Spreading Code	1	-1	1	-1	-1	1	-1	1	1	-1	1	-1	-1	1	-1	1
=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=
Demod	5	0	3	-2	-3	7	-3	2	3	-6	5	-4	-4	3	-5	5
Add these	└───────┬───────┘ / +								└───────┬───────┘ / +
Total	9								-3
1 or -1?
11

---
Example RX
BAND	5	0	3	2	3	7	3	2	3	6	5	4	4	2	5	5
x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x	x
Spreading Code	1	-1	1	-1	-1	1	-1	1	1	-1	1	-1	-1	1	-1	1
=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=	=
Demod	5	0	3	-2	-3	7	-3	2	3	-6	5	-4	-4	3	-5	5
Add these	└───────┬───────┘ / +								└───────┬───────┘ / +
Total	9								-3
1 or -1?	1								-1
11
12

---
Step 13: Find The Letter.
Write it in box 13
Letter	Data
	2	3	4	5	6
A	1	1	1	1	1
B	1	1	1	1	-1
C	1	1	1	-1	1
D	1	1	1	-1	-1
E	1	1	-1	1	1
F	1	1	-1	1	-1
G	1	1	-1	-1	1
H	1	1	-1	-1	-1
I	1	-1	1	1	1
J	1	-1	1	1	-1
K	1	-1	1	-1	1
L	1	-1	1	-1	-1
M	1	-1	-1	1	1
Letter	Data
	2	3	4	5	6
N	1	-1	-1	1	-1
O	1	-1	-1	-1	1
P	1	-1	-1	-1	-1
Q	-1	1	1	1	1
R	-1	1	1	1	-1
S	-1	1	1	-1	1
T	-1	1	1	-1	-1
U	-1	1	-1	1	1
V	-1	1	-1	1	-1
W	-1	1	-1	-1	1
X	-1	1	-1	-1	-1
Y	-1	-1	1	1	1
Z	-1	-1	1	1	-1

---
Step 14:
Work out what went wrong? :-(
Congratulate yourselves! :-)

---
CDMA Transceiver Block Diagram

---
CDMA Transceiver Block Diagram

---
CDMA Transceiver Block Diagram

---
CDMA Transceiver Block Diagram

---
CDMA Transmitter Block Diagram

---
A visual example
Data x Spreading Code = CDMA
 1
x
 1
=
 1
 1
x
-1
=
-1
-1
x
 1
=
-1
-1
x
 -1
=
 1

---
A visual example
Data x Spreading Code = CDMA
 1
x
 1
=
 1
 1
x
-1
=
-1
-1
x
 1
=
-1
-1
x
 -1
=
 1

---
A visual example
Data x Spreading Code = CDMA
 1
x
 1
=
 1
 1
x
-1
=
-1
-1
x
 1
=
-1
-1
x
 -1
=
 1

---
A visual example

---
A visual example
De-
mod
De-
mod
Band
Code
Code
r
De-
mod
De-
mod
Band

---
This has been:
An Introduction to CDMA
Spread-Spectrum
Thanks!
© 2010 Nick Waterman VA3NNW

---
This has been:
An Introduction to CDMA
Spread-Spectrum
Questions?
© 2010 Nick Waterman VA3NNW

---
Supplemental Material

---
Ham CDMA? Kinda? MT63-2000?

---
Ham CDMA? Kinda? MT63-2000?